# Design Specification for R-Sort
The R-sorter (R_sort) component takes an array A of unsigned integers as input and outputs the numbers as an array S sorted by value. There is also a data-ready output DR, which is set to 1 only when the data in output array S is sorted. Other inputs are CLK and RST, for clock and reset signal respectively. The reset signal is asynchronous. Below, in Figure 1, is a schematic overview of the R_sort component.

Figure 1: R_sort component overview
R_sort

A
CLK
RST
S
DR

L

L

Internally, the radix sort algorithm is used for sorting.